## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #18
MSI Components

## Slide 2: Lecture #18: MSI Components
Introduction
Decoders
Encoders
Demultiplexers
Multiplexers

## Slide 3: 1. Introduction (1/2)
An integrated circuit (referred to as an IC, a chip or a microchip) is a set of electronic circuits on one small flat piece (or ‘chip’) of semiconductor material.
Scale of integration: the number of components fitted into a standard size IC
Name | Signification | Year | #transistors | #logic gates
SSI | Small-scale integration | 1964 | 1 to 10 | 1 to 12
MSI | Medium-scale integration | 1968 | 10 to 500 | 13 to 99
LSI | Large-scale integration | 1971 | 500 to 20000 | 100 to 9999
VLSI | Very large-scale integration | 1980 | 20k to 1m | 10k to 99999
ULSI | Ultra-large-scale integration | 1984 | 1m and more | 100k and more

## Slide 4: 1. Introduction (2/2)
Four common and useful MSI circuits:
  Decoder
  Demultiplexer
  Encoder
  Multiplexer
Block diagrams of the above MSI circuits:
decoder
code
entity
encoder
code
entity
mux
data
input
select
demux
data
output
select

## Slide 5: 2. Decoders (1/5)
Codes are frequently used to represent entities, eg: your name is a code to denote yourself (an entity!)
These codes can be identified (or decoded) using a decoder. Given a code, identify the entity.
Convert binary information from n input lines to (a maximum of) 2n output lines.
Known as n-to-m-line decoder, or simply n:m or nm decoder (m  2n).
May be used to generate 2n minterms of n input variables.

## Slide 6: 2. Decoders (2/5)
Example: If codes 00, 01, 10, 11 are used to identify four light bulbs, we may use a 2-bit decoder.
2x4
DEC
2-bit code
X
Y
F0 F1 F2 F3
Bulb 0
Bulb 1
Bulb 2
Bulb 3
This is a 24 decoder which selects an output line based on the 2-bit code supplied.
Truth table:
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 7: 2. Decoders (3/5)
From truth table, circuit for 24 decoder is:
F0 = X'Y'
F1 = X'Y
F2 = XY'
F3 = XY
X
Y
Note: Each output is a minterm (X'Y', X'Y, XY' or XY) of a 2-variable function
X | Y | F0 | F1 | F2 | F3
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1

## Slide 8: 2. Decoders (4/5)
Design a 38 decoder.
F1 = x'y'z
x
z
y
F0 = x'y'z'
F2 = x'yz'
F3 = x'yz
F5 = xy'z
F4 = xy'z'
F6 = xyz'
F7 = xyz
x | y | z | F0 | F1 | F2 | F3 | F4 | F5 | F6 | F7
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 9: 2. Decoders (5/5)
In general, for an n-bit code, a decoder could select up to 2n lines:
:
:
n-bit
code
n to 2n
decoder
up to 2n
output lines

## Slide 10: 2. Decoders: Implementing Functions (1/3)
A Boolean function, in sum-of-minterms form a
  decoder to generate the minterms, and
  an OR gate to form the sum.
Any combinational circuit with n inputs and m outputs can be implemented with an n:2n decoder with m OR gates.
Good when circuit has many outputs, and each function is expressed with a few minterms.

## Slide 11: 2. Decoders: Implementing Functions (2/3)
Example: Full adder
  S(x, y, z) = S m(1,2,4,7)
  C(x, y, z) = S m(3,5,6,7)
3x8
DEC
S2
S1
S0
x
y
z
0
1
2
3
4
5
6
7
S
C

## Slide 12: 2. Decoders: Implementing Functions (3/3)

3x8
DEC
S2
S1
S0
x
y
z
0
1
2
3
4
5
6
7
S
C
1
0
0
0
0
0
0
0
0
0
0
0
0
  S(x, y, z) = S m(1,2,4,7)
  C(x, y, z) = S m(3,5,6,7)

## Slide 13: 2. Decoders with Enable (1/2)
Decoders often come with an enable control signal, so that the device is only activated when the enable, E = 1.
Truth table:
Circuit of a 24 decoder with enable:
X
Y
F0 = EX'Y'
F1 = EX'Y
F2 = EXY'
F3 = EXY
E
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0

## Slide 14: 2. Decoders with Enable (2/2)
In the previous slide, the decoder has a one-enable control signal, i.e. the decoder is enabled with E=1.
In most MSI decoders, enable signal is zero-enable, usually denoted by E' or Ē. The decoder is enabled when the signal is zero (low).
Decoder with 1-enable
Decoder with 0-enable
E | X | Y | F0 | F1 | F2 | F3
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
0 | d | d | 0 | 0 | 0 | 0
E' | X | Y | F0 | F1 | F2 | F3
0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0 | 0 | 1
1 | d | d | 0 | 0 | 0 | 0

## Slide 15: 2. Constructing Larger Decoders (1/4)
Larger decoders can be constructed from smaller ones.
Example: A 38 decoder can be built from two 24 decoders (with one-enable) and an inverter.
3x8
DEC
S2
S1
S0
w
x
y
0
1
:
:
7
F0 = w'x'y'
F1 = w'x'y
:
:
F7 = wxy
2x4
DEC
S1
S0
0
1
2
3
F0 = w'x'y'
F1 = w'x'y
F2 = w'xy'
F3 = w'xy
E
2x4
DEC
S1
S0
0
1
2
3
F4 = wx'y'
F5 = wx'y
F6 = wxy'
F7 = wxy
E
w
x
y

## Slide 16: 2. Constructing Larger Decoders (2/4)

0
1
2
3
2x4
Dec
S1
S0
0
1
2
3
F0 = w'x'y'
F1 = w'x'y
F2 = w'xy'
F3 = w'xy
E
2x4
Dec
S1
S0
F4 = wx'y'
F5 = wx'y
F6 = wxy'
F7 = wxy
E
w
x
y
3x8
Dec
S2
S1
S0
w
x
y
0
1
:
:
7
F0 = w'x'y'
F1 = w'x'y
:
:
F7 = wxy
0
0
0
0
0
0
0
1
0
0
0
1
0

## Slide 17: 2. Constructing Larger Decoders (3/4)
Construct a 416 decoder from two 38 decoders with one-enable and an inverter.
4x16
DEC
S3
S2
S1
S0
w
x
y
z
0
1
:
:
15
F0
F1
:
:
F15
3x8
DEC
S2
S1
S0
0
1
:
7
F0
F1
:
F7
E
3x8
DEC
S2
S1
S0
0
1
:
7
F8
F9
:
F15
E
w
x
y
z
Note: The input w and its complement w' are used to select either one of the two smaller decoders.

## Slide 18: 2. Constructing Larger Decoders (4/4)
Exercise: What modifications should be made to provide an ENABLE input for the 38 decoder and the 416 decoder created in the previous two examples?
Exercise: How to construct a 416 decoder using five 24 decoders with enable?
Decoders may also have zero-enable and/or negated outputs. (See next two slides.)
  Normal outputs = active high outputs
  Negated outputs = active low outputs

## Slide 19: 2. Standard MSI Decoder (1/2)
74138 (3-to-8 decoder)
74138 decoder module.
(a) Logic circuit.
(b) Package pin configuration.

## Slide 20: 2. Standard MSI Decoder (2/2)
74138 decoder module.
(d) Generic symbol.
(e) IEEE standard logic symbol.
Source:The Data Book Volume 2, Texas Instruments Inc.,1985
74138 decoder module.
(c) Function table.
(c)

## Slide 21: 2. Decoders: Implementing Functions Revisit (1/2)
Example: Implement the following function using a 38 decoder and an appropriate logic gate
  f(Q,X,P) =  m(0,1,4,6,7) =  M(2,3,5)
We may implement the function in several ways:
  Using a decoder with active-high outputs with an OR gate: f(Q,X,P) = m0 + m1 + m4 + m6 + m7
  Using a decoder with active-low outputs with a NAND gate: f(Q,X,P) = (m0'  m1'  m4'  m6'  m7' )'
  Using a decoder with active-high outputs with a NOR gate: f(Q,X,P) = (m2 + m3 + m5 )' [ = M2  M3  M5 ]
  Using a decoder with active-low outputs with an AND gate: f(Q,X,P) = m2'  m3'  m5'

## Slide 22: 2. Decoders: Implementing Functions Revisit (2/2)
f(Q,X,P) = Sm(0,1,4,6,7) =  M(2,3,5)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(a) Active-high decoder with OR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(b) Active-low decoder with NAND gate.
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
f(Q,X,P)
(c) Active-high decoder with NOR gate.
f(Q,X,P)
3x8
Dec
A
B
C
Q
X
P
0
1
2
3
4
5
6
7
(d) Active-low decoder with AND gate.
(m0'·m1'·m4'·m6'·m7)'
=m0+m1+m4+m6+m7
(m2+m3+m5)'
= m2'·m3'·m5'
= M2·M3·M5
m2'·m3'·m5'
= M2·M3·M5

## Slide 23: Reading
Reducing Decoders
  Read up DLD pages 136 – 140.

## Slide 24: 3. Encoders (1/4)
Encoding is the converse of decoding.
Given a set of input lines, of which exactly one is high and the rest are low, the encoder provides a code that corresponds to that high input line.
Contains 2n (or fewer) input lines and n output lines.
Implemented with OR gates.
Example:
4-to-2 Encoder
F0
F1
F2
F3
D0
D1
Select via switches
2-bits code

## Slide 25: 3. Encoders (2/4)
Truth table:

With K-map, we obtain:
  D0 = F1 + F3 D1 = F2 + F3
Circuit:
Simple 4-to-2 encoder
?

## Slide 26: 3. Encoders (3/4)
Example: 8-to-3 encoder.
  At any one time, only one input line of an encoder has a value of 1 (high), the rest are zeroes (low).
  To allow for more than one input line to carry a 1,we need priority encoder.

## Slide 27: 3. Encoders (4/4)
Example: 8-to-3 encoder.
An 8-to-3 encoder
D0
D1
D2
D3
D4
D5
D6
D7
z = D1 + D3 + D5 + D7
y = D2 + D3 + D6 + D7
x = D4 + D5 + D6 + D7
Exercise: Can you design a 2n-to-n encoder without using K-map?

## Slide 28: 3. Priority Encoders (1/2)
A priority encoder is one with priority
  If two or more inputs or equal to 1, the input with the highest priority takes precedence.
  If all inputs are 0, this input combination is considered invalid.
Example of a 4-to-2 priority encoder:
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1

## Slide 29: 3. Priority Encoders (2/2)
Understanding “compact” function table
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
X | 1 | 0 | 0 | 0 | 1 | 1
X | X | 1 | 0 | 1 | 0 | 1
X | X | X | 1 | 1 | 1 | 1
Inputs |  |  |  | Outputs |  | 
D0 | D1 | D2 | D3 | f | g | V
0 | 0 | 0 | 0 | X | X | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 0 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Exercise: Obtain the simplified expressions for f, g and V.


## Slide 30: Multiplexers and Demultiplexers
An application:
Helps share a single communication line among a number of devices.
At any time, only one source and one destination can use the communication line.

## Slide 31: 4. Demultiplexers (1/2)
Given an input line and a set of selection lines, a demultiplexer directs data from the input to one selected output line.
Example: 1-to-4 demultiplexer.
demux
Data D
Outputs
select
S1 S0
Y0 = D∙S1'∙S0'
Y1 = D∙S1'∙S0
Y2 = D∙S1∙S0'
Y3 = D∙S1∙S0

## Slide 32: 4. Demultiplexers (2/2)
It turns out that the demultiplexer circuit is actually identical to a decoder with enable.
24 Decoder
D
S1
S0
Y0 = ?
Y1 = ?
Y2 = ?
Y3 = ?
E
A
B
0
1
2
3

demux
Data D
Outputs
select
S1 S0
Y0 = D∙S1'∙S0'
Y1 = D∙S1'∙S0
Y2 = D∙S1∙S0'
Y3 = D∙S1∙S0

## Slide 33: 5. Multiplexers (1/4)
A multiplexer is a device that has
  A number of input lines
  A number of selection lines
  One output line
It steers one of 2n inputs to a single output line, using n selection lines. Also known as a data selector.
2n:1
Multiplexer
output
inputs
:
select
...

## Slide 34: 5. Multiplexers (2/4)
Truth table for a 4-to-1 multiplexer:
4:1mux
Y
Inputs
select
S1 S0
I0
I1
I2
I3
4:1
MUX
Y
Inputs
select
S1 S0
I0
I1
I2
I3
0
1
2
3
Output

## Slide 35: 5. Multiplexers (3/4)
Output of multiplexer is
  “sum of the (product of data lines and selection lines)”
Example: Output of a 4-to-1 multiplexer is:
  Y = ?
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
Note:
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3
This is useful later (eg: slide 45).

## Slide 36: 5. Multiplexers (4/4)
A 4:1 multiplexer circuit:
S1
S0
0 1 2 3
2-to-4 Decoder
I0
I1
I2
I3
Y
S1
S0
I0
I1
I2
I3
Y
A 2n-to-1-line multiplexer, or simply 2n:1 MUX, is made from an n:2n decoder by adding to it 2n input lines, one to each AND gate.

## Slide 37: 5. Multiplexer IC Package
Some IC packages have a few multiplexers in each package (chip). The selection and enable inputs are common to all multiplexers within the package.
S
(select)
A0
A1
A2
A3
B0
B1
B2
B3
E'
(enable)
Y0
Y1
Y2
Y3
Quadruple 2:1 multiplexer

## Slide 38: 5. Constructing Larger Multiplexers (1/4)
Larger multiplexers can be constructed from smaller ones.
An 8-to-1 multiplexer can be constructed from smaller multiplexers like this (note placement of selector lines):
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y

## Slide 39: 5. Constructing Larger Multiplexers (2/4)
4:1 MUX
I0
I1
I2
I3
S1 S0
4:1 MUX
I4
I5
I6
I7
S1 S0
2:1 MUX
S2
Y
When S2S1S0 = 000
I0
I4
I0
When S2S1S0 = 001
I1
I5
I1
When S2S1S0 = 110
I2
I6
I6

## Slide 40: 5. Constructing Larger Multiplexers (3/4)
Another implementation of an 8-to-1 multiplexer using smaller multiplexers:
4:1 MUX
S2 S1
I0
I1
2:1 MUX
S0
I2
I3
2:1 MUX
S0
I4
I5
2:1 MUX
S0
I6
I7
2:1 MUX
S0
Y
I0
When
S2S1S0 = 000
I0
I4
I2
I6
Q: Can we use only 2:1 multiplexers?
0
0
0
0
0 0
S2S1S0 = 101
1
1
1
1
1 0
I1
I5
I3
I7
I5

## Slide 41: 5. Constructing Larger Multiplexers (4/4)
A 16-to-1 multiplexer can be constructed from five 4-to-1 multiplexers:

## Slide 42: 5. Standard MSI Multiplexer (1/2)
74151A 8-to-1 multiplexer. (a) Package configuration. (b) Function table.
(b)

## Slide 43: 5. Standard MSI Multiplexer (2/2)
74151A 8-to-1 multiplexer. (c) Logic diagram. (d) Generic logic symbol. (e) IEEE standard logic symbol.
Source: The TTL Data Book Volume 2. Texas Instruments Inc.,1985.
(c)

## Slide 44: 5. Multiplexers: Implementing Functions (1/3)
Boolean functions can be implemented using multiplexers.
A 2n-to-1 multiplexer can implement a Boolean function of n input variables, as follows:
  1. Express in sum-of-minterms form.
  Example: F(A,B,C) = A'B'C + A'BC + AB'C + ABC' = S m(1,3,5,6)
  2. Connect n variables to the n selection lines.
  3. Put a ‘1’ on a data line if it is a minterm of the function, or ‘0’ otherwise.

## Slide 45: 5. Multiplexers: Implementing Functions (2/3)
F(A,B,C) = S m(1,3,5,6)
mux
A B C
0
1
2
3
4
5
6
7
0
1
0
1
0
1
1
0
F
This method works because:
Output = I0m0 + I1m1 + I2m2 + I3m3 + I4m4 + I5m5 + I6m6 + I7m7
Supplying ‘1’ to I1,I3,I5,I6 , and ‘0’ to the rest:
Output = m1 + m3 + m5 + m6
From slide 34 (4:1 mux)
Expressing
I0∙(S1'∙S0') + I1∙(S1'∙S0) + I2∙(S1∙S0') + I3∙(S1∙S0)
in minterms notation, it is equal to
I0∙m0 + I1∙m1 + I2∙m2 + I3∙m3

## Slide 46: 5. Multiplexers: Implementing Functions (3/3)
Example: Use a 74151A to implement f(x1,x2,x3) = S m(0,2,3,5)
Realization of f(x1,x2,x3) = m(0,2,3,5).
(a) Truth table.
(b) Implementation with 74151A.

## Slide 47: 5. Using Smaller Multiplexers (1/6)
Earlier, we saw how a 2n-to-1 multiplexer can be used to implement a Boolean function of n (input) variables.
However, we can use a single smaller 2(n-1)-to-1 multiplexer to implement a Boolean function of n (input) variables.
Example: The function F(A,B,C) = S m(1,3,5,6) can be implemented using a 4-to-1 multiplexer (rather than an 8-to-1 multiplexer).

## Slide 48: 5. Using Smaller Multiplexers (2/6)
Let’s look at this example:
  F(A,B,C) = S m(0,1,3,6) = A'B'C' + A'B'C + A'BC + ABC'
mux
A B C
0
1
2
3
4
5
6
7
1
1
0
1
0
0
1
0
F
mux
A B
0
1
2
3
1
C
0
C'
F
Note: Two of the variables, A and B, are applied as selection lines of the multiplexer, while the inputs of the multiplexer contain 1, C, 0 and C'.

## Slide 49: 5. Using Smaller Multiplexers (3/6)
Procedure
  1. Express Boolean function in sum-of-minterms form. Example: F(A,B,C) = S m(0,1,3,6)
  2. Reserve one variable (in our example, we take the least significant one) for input lines of multiplexer, and use the rest for selection lines. Example: C is for input lines; A and B for selection lines.

## Slide 50: 5. Using Smaller Multiplexers (4/6)

  3. Draw the truth table for function, by grouping inputs by selection line values, then determine multiplexer inputs by comparing input line (C) and function (F) for corresponding selection line values.
A | B | C | F | MUX input
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 1 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
mux
A B
0
1
2
3
?
?
?
?
F

## Slide 51: 5. Using Smaller Multiplexers (5/6)

Alternative: What if we use A for input lines, and B, C for selector lines?
A' (when BC = 00)
mux
B C
0
1
2
3
?
?
?
?
F

## Slide 52: 5. Using Smaller Multiplexers (6/6)
Example: Implement the function below with 74151A:
  f(x1,x2,x3,x4) = S m(0,1,2,3,4,9,13,14,15)

## Slide 53: Peeking Ahead
1K x 8
DATA (8)
ADRS (10)
CS
RW
Read/write
(8)
Output data
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
0–1023
1024 – 2047
2048 – 3071
3072 – 4095
Input data
8 lines
0
1
2
3
2x4 decoder
Lines
Lines
0 – 9
11 10
S0
S1
Address

## Slide 54: End of File