## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #19
Sequential Logic

## Slide 2: Lecture #19: Sequential Logic (1/2)
Introduction
Memory Elements
Latches
3.1 S-R Latch
3.2 D Latch
Flip-flops
4.1 S-R Flip-flop
4.2 D Flip-flop
4.3 J-K Flip-flop
4.4 T Flip-flop

## Slide 3: Lecture #19: Sequential Logic (2/2)
Asynchronous Inputs
Synchronous Sequential Circuit
6.1 Flip-flop Characteristic Tables
6.2 Analysis
6.3 Flip-flop Excitation Tables
6.4 Design
Memory
7.1 Memory Unit
7.2 Read/Write Operations
7.3 Memory Cell
7.4 Memory Arrays

## Slide 4: 1. Introduction (1/2)
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 5: 1. Introduction (2/2)
Two types of sequential circuits:
  Synchronous: outputs change only at specific time
  Asynchronous: outputs change at any time
Multivibrator: a class of sequential circuits
  Bistable (2 stable states)
  Monostable or one-shot (1 stable state)
  Astable (no stable state)
Bistable logic devices
  Latches and flip-flops.
  They differ in the methods used for changing their state.

## Slide 6: 2. Memory Elements (1/3)
Memory element: a device which can remember value indefinitely, or change value on command from its inputs.
command
Memory element
stored value
Q
Characteristic table:
Q(t) or Q: current state
Q(t+1) or Q+: next state

## Slide 7: 2. Memory Elements (2/3)
Memory element with clock.
Clock is usually a square wave.
command
Memory element
stored value
Q
clock
Positive edges
Negative edges
Positive pulses

## Slide 8: 2. Memory Elements (3/3)
Two types of triggering/activation
  Pulse-triggered
  Edge-triggered
Pulse-triggered
  Latches
  ON = 1, OFF = 0
Edge-triggered
  Flip-flops
  Positive edge-triggered (ON = from 0 to 1; OFF = other time)
  Negative edge-triggered (ON = from 1 to 0; OFF = other time)
Positive edges
Negative edges
Positive pulses

## Slide 9: 3.1 S-R Latch (1/3)
Two inputs: S and R.
Two complementary outputs: Q and Q'.
  When Q = HIGH, we say latch is in SET state.
  When Q = LOW, we say latch is in RESET state.
For active-high input S-R latch (also known as NOR gate latch)
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Outputs Q and Q' are both LOW (invalid!)
Drawback: invalid condition exists and must be avoided.

## Slide 10: 3.1 S-R Latch (2/3)
Active-high input S-R latch:
R
S
Q
Q'
1
0
0
1
1
0
0
0
0
1
1
0
0
1
0
0
1
1
0
0
S
R
Q
Q'
Block diagram:
Notes: Need trace the inputs around 3 times to be sure Q ad Q’ are stable.

## Slide 11: 3.1 S-R Latch (3/3)
Characteristic table for active-high input S-R latch:
S
R
Q
Q'
Q(t+1) = ?

S + R'∙Q
S∙R = 0

## Slide 12: 3.1 Active-Low S-R Latch
(You may skip this slide.)
What we have seen is active-high input S-R latch.
There are active-low input S-R latches, where NAND gates are used instead. See diagram on the left below.
S
R
Q
Q'
In this case,
  when R=0 and S=1, the latch is reset (i.e. Q becomes 0)
  when R=1 and S=0, the latch is set (i.e. Q becomes 1)
  when S=R=1, it is a no-change command.
  when S=R=0, it is an invalid command.
Sometimes, we use the alternative gate diagram for the NAND gate. See diagram on the right above. (This appears in more complex latches/flip-flops in the later slides.)
S
R
Q
Q'
(Sometimes, the inputs are labelled as S' and R'.)

## Slide 13: 3.1 Gated S-R Latch
S-R latch + enable input (EN) and 2 NAND gates  a gated S-R latch.
S
R
Q
Q'
EN
S
EN
R
Q
Q'
Outputs change (if necessary) only when EN is high.

## Slide 14: 3.2 Gated D Latch (1/2)
Make input R equal to S'  gated D latch.
D latch eliminates the undesirable condition of invalid state in the S-R latch.
D
EN
Q
Q'
D
Q
Q'
EN

## Slide 15: 3.2 Gated D Latch (2/2)
When EN is high,
  D = HIGH  latch is SET
  D = LOW  latch is RESET
Hence when EN is high, Q “follows” the D (data) input.
When EN=1, Q(t+1) = ?

D
Characteristic table:

## Slide 16: 4. Flip-flops (1/2)
Flip-flops are synchronous bistable devices.
Output changes state at a specified point on a triggering input called the clock.
Change state either at the positive (rising) edge, or at the negative (falling) edge of the clock signal.
Positive edges
Negative edges
Clock signal

## Slide 17: 4. Flip-flops (2/2)
S-R flip-flop, D flip-flop, and J-K flip-flop.
Note the “>” symbol at the clock input.
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Negative edge-triggered flip-flops
Notes: Functionally, positive or negative no difference

## Slide 18: 4.1 S-R Flip-flop
S-R flip-flop: On the triggering edge of the clock pulse,
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Invalid!
X = irrelevant (“don’t care”)
 = clock transition LOW to HIGH
S
C
R
Q
Q'
Characteristic table of positive edge-triggered S-R flip-flop:

## Slide 19: 4.2 D Flip-flop (1/2)
D flip-flop: Single input D (data). On the triggering edge of the clock pulse,
  D = HIGH  Q becomes HIGH (SET state)
  D = LOW  Q becomes LOW (RESET state)
Hence, Q “follows” D at the clock edge.
A positive edge-triggered D flip-flop formed with an S-R flip-flop.
S
C
R
Q
Q'
CLK
D
 = clock transition LOW to HIGH
Convert S-R flip-flop into a D flip-flop: add an inverter.

## Slide 20: 4.2 D Flip-flop (2/2)
Application: Parallel data transfer.
  To transfer logic-circuit outputs X, Y, Z to flip-flops Q1, Q2 and Q3 for storage.
* After occurrence of negative-going transition
Q1 = X*
D
CLK
Q
Q'
Q2 = Y*
D
CLK
Q
Q'
Q3 = Z*
D
CLK
Q
Q'
Combinational logic circuit
Transfer
X
Y
Z
Notes: To synchronize the 3 logic outputs X,Y,Z to the same clock cycle

## Slide 21: 4.3 J-K Flip-flop (1/2)
J-K flip-flop: Q and Q' are fed back to the pulse-steering NAND gates.
No invalid state.
Include a toggle state
  J = HIGH and K = LOW  Q becomes HIGH (SET state)
  K = HIGH and J = LOW  Q becomes LOW (RESET state)
  Both J and K are LOW No change in output Q
  Both J and K are HIGH Toggle

## Slide 22: 4.3 J-K Flip-flop (2/2)
J-K flip-flop circuit:
J
Q
Q'
CLK
Pulse transition detector
K
Characteristic table:
Q(t+1) = ?
J∙Q' + K'∙Q


## Slide 23: 4.4 T Flip-flop
T flip-flop: Single input version of the J-K flip-flop, formed by tying both inputs together.
Characteristic table:
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T
Q(t+1) = ?

T∙Q' + T'∙Q

## Slide 24: 5. Asynchronous Inputs (1/2)
S-R, D and J-K inputs are synchronous inputs, as data on these inputs are transferred to the flip-flop’s output only on the triggered edge of the clock pulse.
Asynchronous inputs affect the state of the flip-flop independent of the clock; example: preset (PRE) and clear (CLR) [or direct set (SD) and direct reset (RD)].
When PRE=HIGH, Q is immediately set to HIGH.
When CLR=HIGH, Q is immediately cleared to LOW.
Flip-flop in normal operation mode when both PRE and CLR are LOW.

## Slide 25: 5. Asynchronous Inputs (2/2)
A J-K flip-flop with active-low PRESET and CLEAR asynchronous inputs.
J
Q
Q'
CLK
Pulse transition detector
K
PRE
CLR
J
C
K
Q
Q'
PRE
CLR
PRE
CLR
CLK
Q
Preset
Toggle
Clear
J = K = HIGH

## Slide 26: 6. Synchronous Sequential Circuits
Building blocks: logic gates and flip-flops.
Flip-flops make up the memory while the gates form one or more combinational sub-circuits.
We have discussed S-R flip-flop, J-K flip-flop, D flip-flop and T flip-flop.

## Slide 27: 6.1 Flip-flop Characteristic Tables
Each type of flip-flop has its own behaviour, shown by its characteristic table.

## Slide 28: 6.2 Sequential Circuits: Analysis (1/7)
Given a sequential circuit diagram, we can analyze its behaviour by deriving its state table and hence its state diagram.
Requires state equations to be derived for the flip-flop inputs, as well as output functions for the circuit outputs other than the flip-flops (if any).
We use A(t) and A(t+1) (or simply A and A+) to represent the present state and next state, respectively, of a flip-flop represented by A.

## Slide 29: 6.2 Sequential Circuits: Analysis (2/7)
Example using D flip-flops
State equations:
A+ = A∙x + B∙x
B+ = A'∙x
Output function:
y = (A + B)∙x'
Figure 1
A
A'
B
B'
y
x
CP
D
Q
Q'
D
Q
Q'

## Slide 30: 6.2 Sequential Circuits: Analysis (3/7)
From the state equations and output function, we derive the state table, consisting of all possible binary combinations of present states and inputs.
State table
  Similar to truth table.
  Inputs and present state on the left side.
  Outputs and next state on the right side.
m flip-flops and n inputs  2m+n rows.

## Slide 31: 6.2 Sequential Circuits: Analysis (4/7)
State table for circuit of Figure 1:
State equations:
A+ = A∙x + B∙x
B+ = A'∙x
Output function:
y = (A + B)∙x'

## Slide 32: 6.2 Sequential Circuits: Analysis (5/7)
Alternative form of state table:
Full table
Compact table

## Slide 33: 6.2 Sequential Circuits: Analysis (6/7)
From the state table, we can draw the state diagram.
State diagram
  Each state is denoted by a circle.
  Each arrow (between two circles) denotes a transition of the sequential circuit (a row in state table).
  A label of the form a/b is attached to each arrow where a (if there is one) denotes the inputs while b (if there is one) denotes the outputs of the circuit in that transition.
Each combination of the flip-flop values represents a state. Hence, m flip-flops  up to 2m states.

## Slide 34: 6.2 Sequential Circuits: Analysis (7/7)
State diagram of the circuit of Figure 1:
00
01
11
10
1/0
1/0
1/0
0/1
0/1
0/0
1/0
0/1
DONE!
Notes: Label of arrow: Input/output (x/y)

## Slide 35: 6.2 Flip-flop Input Functions (1/3)
The outputs of a sequential circuit are functions of the present states of the flip-flops and the inputs. These are described algebraically by the circuit output functions.
  In Figure 1: y = (A + B)∙x'
The part of the circuit that generates inputs to the flip-flops are described algebraically by the flip-flop input functions (or flip-flop input equations).
The flip-flop input functions determine the next state generation.
From the flip-flop input functions and the characteristic tables of the flip-flops, we obtain the next states of the flip-flops.

## Slide 36: 6.2 Flip-flop Input Functions (2/3)
Example: circuit with a JK flip-flop.
We use 2 letters to denote each flip-flop input: the first letter denotes the input of the flip-flop (J or K for J-K flip-flop, S or R for S-R flip-flop, D for D flip-flop, T for T flip-flop) and the second letter denotes the name of the flip-flop.
JA = B∙C'∙x + B'∙C∙x'
KA = B + y
A
B
C'
x
B
y
CP
J
Q
Q'
K
B'
C
x'

## Slide 37: 6.2 Flip-flop Input Functions (3/3)
In Figure 1, we obtain the following state equations by observing that Q+ = DQ for a D flip-flop:
  A+ = A∙x + B∙x (since DA = A∙x + B∙x)
  B+ = A'∙x (since DB = A'∙x)
A
A'
B
B'
y
x
CP
D
Q
Q'
D
Q
Q'
Figure 1

## Slide 38: 6.2 Analysis: Example #2 (1/3)
Given Figure 2, a sequential circuit with two J-K flip-flops A and B, and one input x.
Obtain the flip-flop input functions from the circuit:
  JA = B JB = x'
  KA = B∙x' KB = A'∙x + A∙x' = A  x
A
B
x
CP
J
Q
Q'
K
J
Q
Q'
K
Figure 2

## Slide 39: 6.2 Analysis: Example #2 (2/3)
  JA = B JB = x'
  KA = B∙x' KB = A'∙x + A∙x' = A  x
Fill the state table using the above functions, knowing the characteristics of the flip-flops used.
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1

Notes: Use input functions to fill in flip-flop inputs, then use the flip-flop inputs to find next state

## Slide 40: 6.2 Analysis: Example #2 (3/3)
Draw the state diagram from the state table.
00
01
10
11
1
0
1
0
0
1
0
1

Notes: ;No output, so label is only x

## Slide 41: 6.2 Analysis: Example #3 (1/3)
Derive the state table and state diagram of this circuit.
Flip-flop input functions:
  JA = B JB = KB = (A  x)' = A∙x + A'∙x'
  KA = B'
J
Q
Q'
K
J
Q
Q'
K
A
x
CP
B
y
Figure 3

## Slide 42: 6.2 Analysis: Example #3 (2/3)
Flip-flop input functions:
  JA = B JB = KB = (A  x)' = A∙x + A'∙x'
  KA = B'
State table:

0 1
0 0
1 0
1 1
0 0
0 1
1 1
1 0

## Slide 43: 6.2 Analysis: Example #3 (3/3)

State diagram:
00
01
11
10
1/1
1/0
0/1
0/1
1/1
0/0
0/0
1/0

## Slide 44: 6.3 Flip-flop Excitation Tables (1/2)
Analysis: Starting from a circuit diagram, derive the state table or state diagram.
Design: Starting from a set of specifications (in the form of state equations, state table, or state diagram), derive the logic circuit.
Characteristic tables are used in analysis.
Excitation tables are used in design.

## Slide 45: 6.3 Flip-flop Excitation Tables (1/2)
Excitation tables: given the required transition from present state to next state, determine the flip-flop input(s).
JK Flip-flop
SR Flip-flop
D Flip-flop
T Flip-flop

## Slide 46: 6.4 Sequential Circuits: Design
Design procedure:
  Start with circuit specifications – description of circuit behaviour, usually a state diagram or state table.
  Derive the state table.
  Perform state reduction if necessary.
  Perform state assignment.
  Determine number of flip-flops and label them.
  Choose the type of flip-flop to be used.
  Derive circuit excitation and output tables from the state table.
  Derive circuit output functions and flip-flop input functions.
  Draw the logic diagram.

## Slide 47: 6.4 Design: Example #1 (1/5)

Given the following state diagram, design the sequential circuit using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
Questions:
How many flip-flops are needed?
How many input variable are there?
Answers:
Two flip-flops. Let’s call them A and B.
One input variable. Let’s call it x.

## Slide 48: 6.4 Design: Example #1 (2/5)

Circuit state/excitation table, using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
JK Flip-flop’s
excitation table.
0 X
0 X
1 X
0 X
X 0
X 0
X 0
X 1
0 X
1 X
X 1
X 0
0 X
1 X
X 0
X 1

## Slide 49: 6.4 Design: Example #1 (3/5)
Block diagram.
What are to go in here?
Combinational
circuit
A'
A
B
B'
x
KA
JA
KB
JB
B
B'
A
A'
External
input(s)
CP
External
output(s)
(none)
J
Q
Q'
K
J
Q
Q'
K

## Slide 50: 6.4 Design: Example #1 (4/5)
From state table, get flip-flop input functions.
A
B
0
1
00 01 11 10
x
A
Bx
X
X
X
X
1
JA = B∙x'
JB = x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
1
KA = B∙x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
KB = (A  x)'
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
1
X
X

## Slide 51: 6.4 Design: Example #1 (5/5)
Flip-flop input functions:
  JA = B∙x' JB = x
  KA = B∙x KB = (A  x)'
Logic diagram:
x
B
A
CP
J
Q
Q'
K
J
Q
Q'
K

## Slide 52: 6.4 Design: Example #2 (1/3)
Using D flip-flops, design the circuit based on the state table below. (Exercise: Design it using JK flip-flops.)

## Slide 53: 6.4 Design: Example #2 (2/3)
Determine expressions for flip-flop inputs and the circuit output y.
DA(A,B,x) = S m(2,4,5,6)
DB(A,B,x) = S m(1,3,5,6)
y(A,B,x) = S m(1,5)
A
B
0
1
00 01 11 10
x
A
Bx
1
1
1
1
A
B
0
1
00 01 11 10
x
A
Bx
1
1
1
1
A
B
0
1
00 01 11 10
x
A
Bx
1
1
DA = A∙B' + B∙x'
DB = A'∙x + B'∙x + A∙B∙x'
y = B'∙x

## Slide 54: 6.4 Design: Example #2 (3/3)
From derived expressions, draw logic diagram:
DA = A∙B' + B∙x'
DB = A'∙x + B'∙x + A.B∙x'
y = B'∙x
D
Q
Q'
D
Q
Q'
A
A'
B
B'
y
CP
x

## Slide 55: 6.4 Design: Example #3 (1/4)
Design involving unused states.
Given these
Derive these
Unused state 000:
Are there other unused states?

## Slide 56: 6.4 Design: Example #3 (2/4)
From state table, obtain expressions for flip-flop inputs.
SA = B∙x
RA = C∙x'
SB = A'∙B'∙x
RB = B∙C + B∙x
B
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
X
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
1
B
X
X
X
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
B
X
X
X
X
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
B
X
X
X
1
X
X
X
X
1
X
X
X
X
1


## Slide 57: 6.4 Design: Example #3 (3/4)

From state table, obtain expressions for flip-flop inputs (cont’d).
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
1
B
X
X
X
X
X
X
X
X
X
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
B
X
X
1
X
X
X
X
1
X
X
B
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
X
X
X
X
X
X
1
SC = x'
RC = x
y = A∙x

## Slide 58: 6.4 Design: Example #3 (4/4)
From derived expressions, draw the logic diagram:
SA = B∙x SB = A'∙B'∙x SC = x' y = A∙x
RA = C∙x' RB = B∙C + B∙x RC = x
A
A'
B
B'
y
CP
x
S
Q
Q'
R
S
Q
Q'
R
S
Q
Q'
R
C

## Slide 59: 7. Memory (1/4)
Memory stores programs and data.
Definitions:
  1 byte = 8 bits
  1 word: in multiple of bytes, a unit of transfer between main memory and registers, usually size of register.
  1 KB (kilo-bytes) = 210 bytes; 1 MB (mega-bytes) = 220 bytes; 1 GB (giga-bytes) = 230 bytes; 1 TB (tera-bytes) = 240 bytes.
Desirable properties: fast access, large capacity, economical cost, non-volatile.
However, most memory devices do not possess all these properties.

## Slide 60: 7. Memory (2/4)
registers
main memory
disk storage
magnetic tapes
Fast, expensive (small numbers), volatile
Slow, cheap (large numbers), non-volatile
Memory hierarchy

## Slide 61: 7. Memory (3/4)
Data transfer
Address
k-bit address bus
0
1
2
3
4
5
Processor
MAR
MDR
Memory
:
n-bit data bus
Control lines
(R/W, etc.)
Up to 2k addressable locations.

## Slide 62: 7. Memory (4/4)
A memory unit stores binary information in groups of bits called words.
The data consists of n lines (for n-bit words). Data input lines provide the information to be stored (written) into the memory, while data output lines carry the information out (read) from the memory.
The address consists of k lines which specify which word (among the 2k words available) to be selected for reading or writing.
The control lines Read and Write (usually combined into a single control line Read/Write) specifies the direction of transfer of the data.

## Slide 63: 7.1 Memory Unit
Block diagram of a memory unit:
Memory unit
2k words
n bits per word
k address lines
k
Read/Write
n
n
n data input lines
n data output lines

## Slide 64: 7.2 Read/Write Operations
Write operation:
  Transfers the address of the desired word to the address lines.
  Transfers the data bits (the word) to be stored in memory to the data input lines.
  Activates the Write control line (set Read/Write to 0).
Read operation:
  Transfers the address of the desired word to the address lines.
  Activates the Read control line (set Read/Write to 1).

## Slide 65: 7.3 Memory Cell
Two types of RAM
  Static RAMs use flip-flops as the memory cells.
  Dynamic RAMs use capacitor charges to represent data. Though simpler in circuitry, they have to be constantly refreshed.
R
S
Q
Input
Select
Output
Read/Write
BC
Output
Input
Select
Read/Write
Logic diagram
Block diagram
A single memory cell of the static RAM has the following logic and block diagrams:

## Slide 66: 7.4 Memory Arrays (1/4)
Logic construction of a 43 RAM (with decoder and OR gates):

## Slide 67: 7.4 Memory Arrays (2/4)
An array of RAM chips: memory chips are combined to form larger memory.
A 1K  8-bit RAM chip:
Block diagram of a 1K x 8 RAM chip
RAM 1K x 8
DATA (8)
ADRS (10)
CS
RW
Input data
Address
Chip select
Read/write
(8)
Output data
8
8
10

## Slide 68: 7.4 Memory Arrays (3/4)
4K  8 RAM.
1K x 8
DATA (8)
ADRS (10)
CS
RW
Read/write
(8)
Output data
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
0–1023
1024 – 2047
2048 – 3071
3072 – 4095
Input data
8 lines
0
1
2
3
2x4 decoder
Lines
Lines
0 – 9
11 10
S0
S1
Address

## Slide 69: 7.4 Memory Arrays (4/4)
2M  32 memory module
  Using 512K  8 memory chips.
Chip select
512K x 8 memory chip
19-bit
address
8-bit data
input/output
19-bit internal chip address
2-bit
decoder
addresses
21-bit
A
0
A
1
A
19
512k X 8
memory chip
A
20
D
31-24
D
7-0
D
23-16
D
15-8
Read/write control line not included in this diagram.

## Slide 70: End of File