## Slide 1: CS2100
Tutorial #3
MIPS ProgrammIng
(Prepared by: Aaron Tan)

## Slide 2
Remember to attempt the discussion question D1 and discuss it on the Forum.

## Slide 3
Q1.
Palindrome
char str[size] = { ... }; // some string
int lo, hi, matched; // matched = 1 (palindrome);
// matched = 0 (not palindrome)
// Translate to MIPS from this point onwards
lo = 0;
hi = size-1;
matched = 1; // assume this is a palindrome
while ((lo < hi) && matched) {
if (str[lo] != str[hi])
matched = 0; // found a mismatch
else {
lo++;
hi--;
}
}
Variable mappings:
lo  $s0;
hi  $s1;
matched  $s3;
Base address of str[]  $s4;
size  $s5
Note:
I’ve shortened the variable names “string”, “low”, “high” to “str”, “lo”, “hi” for brevity.

## Slide 4
Q1.
char str[size] = { ... };
int lo, hi, matched;
lo = 0; hi = size-1; matched = 1;
while ((lo < hi) && matched) {
if (str[lo] != str[hi]) matched = 0;
else { lo++; hi--;
}
}
Variable mappings:
lo  $s0; hi  $s1; matched  $s3;
Base address of str[]  $s4;
size  $s5
# lo = 0
# hi = size-1
# matched = 1
loop: # (lo < hi)?
addi $s0, $zero, 0
addi $s1, $s5, -1
addi $s3, $zero, 1
slt $t0, $s0, $s1
beq $t0, $zero, exit # exit if (lo >= hi)
exit:
beq $s3, $zero, exit # exit if (match == 0)
add $t1, $s4, $s0 # addr of str[lo]
lb $t2, 0($t1) # $t2 = str[lo]
Why do we use lb instead of lw?
Use slt, beq to implement blt.
(blt is a pseudo-instruction; do not use pseudo-instructions)
beq $t2, $t4, else # compare str[lo], str[hi]
add $t3, $s4, $s1 # addr of str[hi]
lb $t4, 0($t3) # $t4 = str[hi]
Study how we load data from memory: (1) prepare address in a register, (2) load using that address (with offset if necessary.)
addi $s3, $zero, 0 # matched = 0
J endW # can also be “j loop”
endW: j loop
else: addi $s0, $s0, 1 # lo++
addi $s1, $s1, -1 # hi--
else:

## Slide 5
Q1.
addi $s0, $zero, 0 # lo = 0
addi $s1, $s5, -1 # hi = size-1
addi $s3, $zero, 1 # matched = 1
loop: slt $t0, $s0, $s1 # (lo < hi)?
beq $t0, $zero, exit # exit if (lo >= hi)
beq $s3, $zero, exit # exit if (match == 0)
add $t1, $s4, $s0 # addr of str[lo]
lb $t2, 0($t1) # $t2 = str[lo]
add $t3, $s4, $s1 # addr of str[hi]
lb $t4, 0($t3) # $t4 = str[hi]
beq $t2, $t4, else # compare str[lo], str[hi]
addi $s3, $zero, 0 # matched = 0
J endW # can also be “j loop”
else: addi $s0, $s0, 1 # lo++
addi $s1, $s1, -1 # hi--
endW: j loop
exit:
add $t1, $s4, $s0 # addr. Of str[lo]
add $t3, $s4, $s1 # addr. Of str[hi]
slt $t0, $t1, $t3 # compare lo and hi addr
addi $t1, $t1, 1 # lo addr increment
addi $t3, $t3, -1 # hi addr decrement
Using “array pointer”.

## Slide 6
Q2.
(a)
Instruction encoding | MIPS code
 | # $s1 stores the results; $t0 stores a non-negative number
 | addi $s1, $zero, 0 #inst addr is 0x00400028
0x00084042 | Loop: srl $t0, $t0, 1
0x11000002 | 
0x22310001 | 
 | j loop
 | exit:
?
?
?
?

## Slide 7
Q2.
(a) addi $s1, $zero, 0
Look up MIPS Reference Data sheet!
Name | Mnemonic | Format | Operation | Opcode/Funct
Add Immediate | addi | I | R[rt] = R[rs] + SignextImm | 8hex
I format:
opcode | rs | rt | immediate
0 0 1 0 0 0
$s1 = $17; $zero = $0
0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
1 0 0 0 1
(2 0 1 1 0 0 0 0)16
Which is rs (source) and which is rt (target)?
rs =
rt =

## Slide 8
Q2.
(a) 0x11000002
0x11000002 = 0001 0001 0000 0000 0000 0000 0000 0010
Opcode = 4
Look up MIPS Reference Data sheet!
Name | Mnemonic | Format | Operation | Opcode/Funct
Branch On Equal | beq | I | If R[rs] == R[rt] PC = PC + 4 + BranchAddr | 4hex
I format:
opcode | rs | rt | immediate
 | MIPS code
 | addi $s1, $zero, 0
0x00084042 | Loop: srl $t0, $t0, 1
0x11000002 | 
0x22310001 | 
 | j loop
 | exit:
beq
$8 = $t0
$t0,
$zero,
2
Next instr.
+2 instr.
exit

## Slide 9
Q2.
(a) 0x22310001
0x22310001 = 0010 0010 0011 0001 0000 0000 0000 0001
Opcode = 8
Look up MIPS Reference Data sheet!
Name | Mnemonic | Format | Operation | Opcode/Funct
Add Immediate | addi | I | R[rt] = R[rs] + SignextImm | 8hex
I format:
opcode | rs | rt | immediate
addi
$17 = $s1
$s1
$s1
____, ____,
1

## Slide 10
Q2.
(a) j loop
Look up MIPS Reference Data sheet!
Name | Mnemonic | Format | Operation | Opcode/Funct
Jump | j | J | PC = JumpAddr | 2hex
J format:
opcode | address
0 0 0 0 1 0
What is the address of the srl instruction?
0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 1
(0 8 1 0 0 0 0 B)16
MIPS code | Address
addi $s1, $zero, 0 | 0x00400028
Loop: srl $t0, $t0, 1 | 
j loop | 
exit: | 
?
0x00400028 + 4 = 0x0040002C
0000 0000 0100 0000 0000 0000 0010 1100
Remove the first 4 bits and last 2 bits:

## Slide 11
Q2.
(a)
Instruction encoding | MIPS code
 | # $s1 stores the results; $t0 stores a non-negative number
 | addi $s1, $zero, 0 #inst addr is 0x00400028
0x00084042 | Loop: srl $t0, $t0, 1
0x11000002 | 
0x22310001 | 
 | j loop
 | exit:
?
?
?
?
0x20110000
beq $t0, $zero, exit
addi $s1, $s1, 1
0x0810000B

## Slide 12
Q2.
(b)
Give a simple mathematic expression for the relationship between $s1 and $t0.
addi $s1, $zero, 0
loop: srl $t0, $t0, 1
beq $t0, $zero, exit
addi $s1, $s1, 1
j loop
exit:

## Slide 13
Q3a.
Binary search
Variable
mappings:
addr. of
array[0]  $s0;
target  $s1;
low  $s2;
high  $s3;
mid  $s4;
ans  $s5.
MIPS code | Comment
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | # while (low <= high) {
add $s4, $s2, $s3 [ ] | # mid = (low + high)/2
sll $t0, $s4, 2 add $t0, $s0, $t0 [ ] | # t0 = mid*4 # t0 = &array[mid] in bytes # t1 = array[mid]
slt $t9, $s1, $t1 beq $t9, $zero, bigger | # if (target < array[mid])
addi $s3, $s4, -1 j lpEnd | # high = mid – 1
bigger:[ ] [ ] | # else if (target > array[mid])
addi $s2, $s4, 1 j lpEnd; | # low = mid + 1
equal: add $s5, $s4, $zero [ ] | # else { ans = mid; break; }
lpEnd: [ ] | #} // end of while loop
end: | 

## Slide 14
Q3a.
Binary search
Variable
mappings:
addr. of
array[0]  $s0;
target  $s1;
low  $s2;
high  $s3;
mid  $s4;
ans  $s5.
MIPS code | Comment
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | # while (low <= high) {
add $s4, $s2, $s3 [ ] | # mid = (low + high)/2
sll $t0, $s4, 2 add $t0, $s0, $t0 [ ] | # t0 = mid*4 # t0 = &array[mid] in bytes # t1 = array[mid]
slt $t9, $s1, $t1 beq $t9, $zero, bigger | # if (target < array[mid])
addi $s3, $s4, -1 j lpEnd | # high = mid – 1
bigger:[ ] [ ] | # else if (target > array[mid])
addi $s2, $s4, 1 j lpEnd; | # low = mid + 1
equal: add $s5, $s4, $zero [ ] | # else { ans = mid; break; }
lpEnd: [ ] | #} // end of while loop
end: | 
srl $s4, $s4, 1
lw $t1, 0($t0)
slt $t9, $t1, $s1
beq $t9, $zero, equal
j end
j loop

## Slide 15
Q3.
MIPS code | Address
loop: slt $t9, $s3, $s2 bne $t9, $zero, end | 0xFFFFFF00
add $s4, $s2, $s3 srl $s4, $s4, 1 | 
sll $t0, $s4, 2 add $t0, $s0, $t0 lw $t1, 0($t0) | 
slt $t9, $s1, $t1 beq $t9, $zero, bigger | 
addi $s3, $s4, -1 j lpEnd | 
bigger: slt $t9, $t1, $s1 beq $t9, $zero, equal | 
addi $s2, $s4, 1 j lpEnd; | 
equal: add $s5, $s4, $zero j end | 
lpEnd: j loop | 
end: | 
(b) What is the immediate value in decimal for the “bne $t9, $zero, end” instruction?
end: is 16 instructions away from bne’s next instruction (add $s4, $2, $s3), so the immediate value is 16.
(c) If the first instruction is at address 0xFFFFFF00, what is the hexadecimal representation of this “j lpEnd”?
Address at lpEnd: is 0xFFFFFF00 + (1710×4) =0xFFFFFF44.
Removing the first 4 bits and last 2 bits, we put this into the immediate field. Opcode of j is 000010. Hence,
000010 1111 1111 1111 1111 1111 0100 01
= 0x0BFFFFD1
(d) Is the encoding of the second “j lpEnd” different from part (c)?
Same encoding. The two j instructions jump to the same address.

## Slide 16
END OF FILE